## Slide 1: Microcontroller experiment and its simulation using Python
Jayesh Gandhi1 and Dr. Vibhuti Joshi2
1. Narmada College of Science and Commerce, Zadeshwar, Bharuch, Gujarat
2. Veer Narmad South Gujarat University, Surat, Gujarat
SCIPY.IN 2010
Hydrabad

## Slide 2: Microcontroller experiment and its simulation using Python
Jayesh Gandhi1 and Dr. Vibhuti Joshi2
1. Narmada College of Science and Commerce, Zadeshwar, Bharuch, Gujarat
2. Veer Narmad South Gujarat University, Surat, Gujarat
SCIPY.IN 2010
Hydrabad

## Slide 3
Microcontroller experiment and its simulation using Python
  Why Microcontrollers ?
  Microcontrollers are programmable electronic device having the following qualities
  Processing power
  High Speed
Scipy.in 2010

## Slide 4
Microcontroller experiment and its simulation using Python
The focus is on developing study modules for microcontroller experiments
Demonstration of the concepts in the class room through simulation
Replicating the same modules with real systems in the laboratories
Our Focus
Scipy.in 2010

## Slide 5
Microcontroller experiment and its simulation using Python
In the present work we have developed two learning experiments
  Interfacing of single seven segment display
  Interfacing of multiplexed seven segment display.
Python is selected for implementing this work, following modules are also used
  vpython for simulation
  pyserial for communication with the microcontroller
Present work
Scipy.in 2010

## Slide 6
Microcontroller experiment and its simulation using Python
Basics of Seven Segment Display:
The common anode is connected to 5 V
and
If `a’ is made zero through a limiting resistor
The LED corresponding ‘a’ will glow
Scipy.in 2010

## Slide 7
Microcontroller experiment and its simulation using Python
Decimal number | Binary number | a | b | c | d | e | f | g
0 | 0000 | on | on | on | on | on | on | 
1 | 0001 |  | on | on |  |  |  | 
2 | 0010 | on | on |  | on | on |  | on
3 | 0011 | on | on | on | on |  |  | on
4 | 0100 |  | on | on |  |  | on | on
5 | 0101 | on |  | on | on |  | on | on
6 | 0110 |  |  | on | on | on | on | on
7 | 0111 | on | on | on |  |  |  | 
8 | 1000 | on | on | on | on | on | on | on
9 | 1001 | on | on | on |  |  | on | on
Selectively glowing LED would display numbers
The table shown indicates the LED to be switched on
to display a number
Scipy.in 2010

## Slide 8
Microcontroller experiment and its simulation using Python
  The First Experiment: Simulation of a Single Display
Simulation program runs on the computer
It communicates data to Microcontroller
Microcontroller sets the port values in binary form
Decoder decodes the value into seven segment format
The value is displayed on the display and the screen
Scipy.in 2010

## Slide 9
Microcontroller experiment and its simulation using Python
Simulation Screen

## Slide 10
Microcontroller experiment and its simulation using Python
Simulation Screen

## Slide 11
Microcontroller experiment and its simulation using Python
The Second Experiment
Simulation of Multiplexed Display
A single digit is not sufficient to display the output from a controller.
Multiple displays would require more microcontroller resources (like ports) and additional hardware.
To optimise the microcontroller resources and reduce the hardware, multiplexing is used.
Scipy.in 2010

## Slide 12
Microcontroller experiment and its simulation using Python
One display is switched on at a time, and the sequence is repeated at a high frequency.
For persistence of vision 16 frames are required in a second.
Scipy.in 2010

## Slide 13
Microcontroller experiment and its simulation using Python
Simulation Program
Four display digits are simulated
First display is made visible with the first number and the others are made invisible (Colored same as background)
Then the second display is switched on with the second number and others are made invisible and so on
Initially the frequency is kept very low which make the idea clear that how the display are switched
Scipy.in 2010

## Slide 14
Microcontroller experiment and its simulation using Python
Simulation Program
With the sliding control the frequency is then increased
Slowly the blinking starts disappearing
At very high frequencies all the four display are visible simultaneously
Scipy.in 2010

## Slide 16
Microcontroller experiment and its simulation using Python
Acknowledgements
University Grants Commission: the present work is a part of minor research project granted by UGC
PHOENIX Project (IUAC Delhi) for introducing me to Open Source Software and Python as programming language
Scipy.in for providing me this opportunity
Scipy.in 2010

## Slide 17
Microcontroller experiment and its simulation using Python
Thank You
Scipy.in 2010